## Slide 1
LOGIC ANALYZER
Module Guide & System Overview
One input, sampled at up to 10 MS/s inside a MAX 10 FPGA — stored in on-chip RAM — read out by an STM32 — displayed on a PC.
MAX 10 FPGA
STM32
PC / Python

## Slide 2
BIG PICTURE
One wire in. A picture on screen.
The whole assignment is one signal chain, built once and proven at every stage before moving on.
FPGA
MAX 10
Samples the probe wire at up to 10 MS/s, finds the trigger, stores the capture in on-chip block RAM.
MCU
STM32
Drains the buffer bit by bit, packs it into bytes, frames it, and streams it out over UART.
PC
Python tool
Verifies the frames, rebuilds the samples, plots the waveform, and can export a VCD file.
The one idea that ties every module together
The FPGA works in samples. The link works in bytes. The PC works in samples again. Packing and unpacking is purely a software transport detail — every module below exists to do one job in one of these domains, or to move data safely across the boundary between them.
Logic Analyzer — Module Guide
2

## Slide 3
ARCHITECTURE
Three subsystems, two interfaces
1
FPGA — capture engine
The only part that touches the probe wire. Built from six small Verilog modules on one sample clock. Finishes when a full buffer sits in block RAM.
2
STM32 — controller & relay
Never touches the probe signal. Drives the FPGA handshake, drains the buffer, frames it, and pushes it out over UART. Most of the project's code lives here.
3
PC tool — verification & display
The only part facing an unreliable link. Checks every frame, reassembles the capture, and turns it into a waveform with cursors and VCD export.
Logic Analyzer — Module Guide
3

## Slide 4
SECTION 1 OF 3
The FPGA: six Verilog modules
~150 lines total. Buffer depth, clock rate and input width all live in one shared parameter file.
1
sync
Resynchronizes every external signal to the sample clock
2
rate_div
Turns the hardware clock into a chosen sample rate
3
trigger
Detects the rising/falling edge that starts a capture
4
capture
IDLE / RUNNING / FULL state machine driving the write
5
buffer
16,384 × 1-bit block RAM holding one capture
6
readout
Address counter that hands samples to the MCU
Logic Analyzer — Module Guide
4

## Slide 5
FPGA MODULE 1 OF 6
1
sync
Input synchronizer — two flip-flops on every signal entering the chip
WHY IT EXISTS
The probe wire, plus the strobe and arm lines from the MCU, are all asynchronous to the FPGA's sample clock. Sampling an asynchronous signal directly risks metastability: an invalid voltage that different downstream logic can resolve differently. Skip this and, in the brief's words, “the instrument becomes a random number generator that occasionally looks right.”
HOW IT'S IMPLEMENTED
Two flip-flops in series sit on every signal entering the chip — the probe input, and the strobe and arm lines from the MCU. The first flip-flop is allowed to go metastable; by the time its output reaches the second flip-flop one clock later, it has almost always settled to a clean, valid level.
Logic Analyzer — The FPGA
5

## Slide 6
FPGA MODULE 2 OF 6
2
rate_div
Sample-rate generator — a clock-enable pulse, not a second clock
WHY IT EXISTS
The FPGA's hardware clock runs far faster than any useful sample rate, and users need to choose between 10 MS/s and 10 kS/s without redesigning the capture logic. Building an actual second, slower clock signal is exactly the kind of gated-clock trick that causes timing-closure and glitch problems on FPGAs.
HOW IT'S IMPLEMENTED
A counter counts up to N and produces a single-cycle sample-enable pulse every N clocks, where N comes from the rate-select input. Every other module simply asks “is this the enable pulse?” — nothing downstream needs to know the actual clock frequency.
WATCH OUT: Divide with an enable pulse, never by building a clock out of logic.
Logic Analyzer — The FPGA
6

## Slide 7
FPGA MODULE 3 OF 6
3
trigger
Edge detector — the event that anchors the capture window
WHY IT EXISTS
A fixed-time capture would rarely land on the interesting part of a signal. The instrument instead needs to recognize a specific event — a rising or falling edge — and use that instant to anchor the whole capture.
HOW IT'S IMPLEMENTED
One flip-flop holds the previous (synchronized) sample; comparing it against the current sample detects the user-selected edge and produces a single trigger pulse. Kept in its own module with one output so it can grow later — pattern or multi-edge triggers can be added without touching anything else.
Logic Analyzer — The FPGA
7

## Slide 8
FPGA MODULE 4 OF 6
4
capture
Capture state machine — IDLE / RUNNING / FULL
WHY IT EXISTS
Something has to decide when the instrument is watching for a trigger, when it is actively recording, and when it is done — and guarantee it stops cleanly even if the trigger never arrives. This is the module that touches nearly every other signal in the design.
HOW IT'S IMPLEMENTED
A three-state machine sits between trigger and buffer. IDLE waits for the trigger pulse; RUNNING writes one sample per enable pulse into the buffer; FULL is reached once the last address is written, raising a done flag for the MCU. An abort input and a timeout stop it sitting armed forever.
Logic Analyzer — The FPGA
8

## Slide 9
FPGA MODULE 5 OF 6
5
buffer
Capture RAM — 16,384 × 1-bit block RAM
WHY IT EXISTS
A captured sample has to be stored somewhere the (much slower, intermittently connected) MCU can retrieve it after the fact. On-chip block RAM lets the capture state machine write at full sample rate with no external dependency.
HOW IT'S IMPLEMENTED
One block RAM, 16,384 addresses deep, one bit wide, written one sample per enable pulse from address 0. Address 0 is defined as the trigger sample, so the RAM address and the sample number are always identical — no arithmetic offset to get wrong. At 10 MS/s this is a 1.6 ms capture window.
Logic Analyzer — The FPGA
9

## Slide 10
FPGA MODULE 6 OF 6
6
readout
MCU-facing address counter — turns the buffer into a bitstream
WHY IT EXISTS
The buffer's contents have to leave the FPGA one bit at a time over a link with only a single data wire — there is no wide parallel bus between the two boards, so the RAM cannot simply be dumped in one operation.
HOW IT'S IMPLEMENTED
A second, independent address counter walks the buffer from address 0 upward. It continuously drives the sample at its current address onto the data pin, and advances only when the MCU pulses rd_strobe — turning the parallel buffer into a strictly MCU-paced serial stream.
Logic Analyzer — The FPGA
10

## Slide 11
INTERFACE 1 OF 2
FPGA ↔ MCU: six wires and a handshake
Signal | Direction | Width | What it does
data | FPGA → MCU | 1 | The sample at the readout module's current address
done | FPGA → MCU | 1 | Capture finished; wired to an STM32 EXTI interrupt
arm | MCU → FPGA | 1 | Pulse to start a new capture and clear the last one
rd_strobe | MCU → FPGA | 1 | Pulse to advance the readout module to the next sample
rate[1:0] | MCU → FPGA | 2 | Sample-rate select (board switches can substitute)
The read cycle
MCU pulses arm — FPGA clears its write pointer, starts watching for the trigger
Trigger fires — 16,384 samples written, done goes high
EXTI handler sets a flag and returns immediately — nothing else runs in the handler
Main loop: read data, shift into a byte, then pulse rd_strobe — read first, advance second
Repeat 16,384 times (2,048 bytes); pulse arm again for the next capture
TWO EASY MISTAKES
Synchronize rd_strobe: it's async to the FPGA clock too — skip it and get an intermittent bug. Bit order: earliest sample = bit 7. Both ends must agree, or captures look almost right.
Logic Analyzer — Interfaces
11

## Slide 12
SECTION 2 OF 3
The MCU: where most of the code lives
Bare-metal register access — not a HAL — for the GPIO, timer and UART paths that matter.
Control lines
Drive arm, rd_strobe and rate-select toward the FPGA
Buffer drain
Read the data pin 16,384×, packing 8 samples per byte
Framing & TX
Wrap bytes into the protocol frame, push out UART
Interrupt handling
done handler only sets a flag and returns
Debug console
UART commands: arm, status, dump, rate, test, repeat
Auto-repeat
Re-arm the instant the last frame has gone out
Self-timing
DWT cycle counter measures drain / transfer / dead time
Test-signal generation
SPI in transmit-only mode drives the self-test pattern
Logic Analyzer — The MCU
12

## Slide 13
INTERFACE 2 OF 2
The link to the PC: UART, 921,600 baud, 8N1
The one link that shares a machine with a general-purpose OS — it can drop or corrupt bytes, so it's the one place that needs a real protocol.
Field | Size | Meaning
SOF | 2 bytes | Start-of-frame marker: 0x55 0xAA
TYPE | 1 byte | CONFIG / ARM / ABORT / STATUS / DATA / ACK / NAK / ERROR
VER | 1 byte | Protocol version, starting at 1
SEQ | 2 bytes | Increments every frame; wraps
LEN | 2 bytes | Payload length in bytes
DATA | LEN bytes | Payload
CRC | 2 bytes | CRC-16-CCITT over TYPE through DATA
WHY IT'S BUILT THIS WAY
A full capture is 2,048 bytes, so it's split across several frames. The PC checks SEQ and CRC on every frame and simply asks again if either is wrong — the FPGA holds the capture until the next arm, so a re-read always works. Framing is kept separate from the UART driver so that moving to USB later only touches the driver, not the framing logic above it.
Logic Analyzer — Interfaces
13

## Slide 14
SECTION 3 OF 3
The PC tool: verify, rebuild, display
1
Configure & arm
Set sample rate and trigger edge, send arm
2
Receive & verify
Check SEQ + CRC per frame; re-request on failure
3
Unpack
Reverse the MCU's bit-packing to one sample/element
4
Decode hook
Empty placeholder — left in the pipeline for later
5
Plot
Rebuild the time axis; zoom, cursors, Δt readout
6
Export / self-test
VCD export, plus a PASS/FAIL regression check
Logic Analyzer — The PC Tool
14

## Slide 15
PROVING IT WORKS
The six-step proof ladder
The MCU generates the test signal AND receives the capture, so it can check itself and print PASS or FAIL — no squinting at waveforms.
1
Ramp
Known pattern through readout, before the capture core exists — proves wiring, strobe, packing, framing, CRC, plotting
2
Static levels
Drive high → all 1s; drive low → all 0s
3
Square wave
100 kHz toggle → exactly 500 samples per run
4
One byte
0xB6 over SPI at 100 kHz → 100 samples/bit, 800 samples/byte
5
Twenty bytes
16,000 samples — a single dropped sample now shows as a visible divergence
6
Push until it breaks
Raise SPI clock until decode fails — record the number for the datasheet
Logic Analyzer — Testing
15

## Slide 16
TIMELINE
Two weeks, four checkpoints
When | What has to work | Watch out for
End of day 3 | Blink from own RTL, SignalTap used once, one module simulated | Losing days to tool setup in silence — ask
End of week 1 | Design doc done, capture core simulating, ramp test on screen | Writing RTL before the design doc exists
Mid week 2 | Real captures, triggered properly, correct time axis | Trusting the plot before the loopback check
End of week 2 | Loopback passing, auto-repeat, VCD, fault handling, datasheet | Leaving measurements until the last afternoon
Done means: board wired up, tool running, twenty-byte loopback prints PASS from your own tooling — then the error rate over a hundred runs.
Logic Analyzer — Timeline
16

## Slide 17
RECAP
Why the design holds together
Every module owns exactly one job in one domain: raw samples inside the FPGA, framed bytes across the two links, and reconstructed samples again on the PC.
sync makes the crossing from an unclocked wire safe. rate_div turns one clock into any sample rate. trigger and capture decide when and how to record. buffer and readout store a capture and hand it out one bit at a time. The MCU bridges that narrow protocol to a checksummed one that survives a shared, unreliable link — and the PC turns it back into the picture the brief promised: clip it onto a wire, hit capture, see what happened.
The test strategy exists to catch the one failure mode that matters most: a capture that looks almost right.